## Slide 1: Flight simulators
Design and production
Borka Danilović,
Senior optical system designer
Technical lead VDS, CAE Inc
Sarajevo, October 2018

## Slide 2
Borka Danilović
Prirodno Matematički Fakultet, Departement of Physics, University of Srajevo
Generation: 1967/68,
Graduated: Dec 1972
Prof. Dr. Krunoslav Ljolje
Ms. Sc. 1997, University of Sherbrooke, Canada
Work Experience: 45 years
“Zrak”, Srajevo, 1973 – 1985
“Unis Institut”, Sarajevo, 1985 – 1992
“CAE Inc”, Montreal, 1996 - 2018

## Slide 3: Designing flight simulator from 1982
CAE Inc
- Senior Optical system Designer
-Technical Lead in Visual Display System (VDS) Group
ZRAK DD
Premium optical and optoelectronic devices and laser devices
Company started in 1948
- Operates using internal ZRAK Standard quality system (ZS)
First flight simulator optical system designed at Zrak Sarajevo
-Senior optical system designer
CAE Inc
“…- Each year we train more than 120,000 civil and defence crewmembers and thousands of healthcare professionals worldwide”
- Over 9,000 employees
- 160 sites and training locations in over 35 countries
Designing flight simulator in 1918

## Slide 4: Flight Simulator industry
Satisfy flying industry needs
Very fast growing demand for new pilots
- general evaluation predicts more than 500000 pilots needed in next 20 years
- according some evaluation 40000 new pilots per year (civil)
New technology for training
Evaluation of virtual reality implementation in a flight training

## Slide 5: Flight Simulator industry
Full flight simulator price, depending of requirements for training, is evaluated
  500.000 USD$ - more than 40 Millions USD$
  Average Full Flight Simulator (FFS) for civil aviation 25 millions USD$
  Average FFS maintenance cost FFS ~1 Million USD$ / year
Consequences
  Very big competition
  Very demanding customers
  Very demanding Flight Simulator regulations for different countries
  - FAA (Federal Aviation Administration - USA)
  - EASA (European Aviation Safety Agency)
  - CASAR (Civil Aviation Safety Regulation - Australia)
  - ICAO (International Civil Aviation Organisation)
  - ……
“The global flight simulator market revenue is expected to reach USD 5.62 billion by 2024..”

## Slide 6
Winning condition for flight simulator design and production
  Very good quality
  Competitive price
  Capacity to support very short schedule
  First time right and on time
  Very good customer support
Certification
-Civil aviation
-The training can be performed only on a flight simulator certified by designated Authorities
Military aviation
-Depending of contract
Flight Simulator industry

## Slide 7: Flight simulators
Research and Development ( R & D ) simulators
- Evaluation of new plain behavior
- A 380 and B 787 simulators were used to confirm the final plain design
- Evaluation of new requirements for flight simulator
Training simulators
- Each type of plain need to have specific simulator
- Flight Training Device (FTD) - fixed training device (lower level training devices)
- Full Flight Simulator (FFS) - motion training device (high level training devices)

## Slide 8: Flight simulators Requirements
Objective / measurable
- Latency
- Field of View (FOV)
- Brightness
- Resolution
- Contrast
Subjective based on perception
- “non distractive” characteristics
- perception of height, depth, distance, …
- smearing (motion blur, dynamic resolution, retinal smearing)
- motion sickness

## Slide 9: physicists are involved in design and production of
Visual System
Motion System
Flight System
Proposals
Design
Design meetings with customer
Testing and testing documentation
Acceptance with customers
Certification with Authorities

## Slide 10: Flight Simulator Visual systems
Display systems
Projection systems
-Blending subsystem
Calibration/ auto-calibration system
Image generators (IGs)
Data Base (DB)

## Slide 11: Flight Simulator Visual Display and projection systems
Different requirements for
- Fixed wings
- Collimated systems
- FOV 200o horizontal x 40o vertical (per standard)
- Helicopters
- Collimated or direct projection systems
- FOV 180o horizontal x 60o vertical (per standard)
High brightness (illuminance) at Pilot Eye Point (PEP) or Co-pilot Eye Point (CEP)
High resolution at PEP and CEP
High contrast
Realistic perception
Customer are demanding more than prescribed minimum

## Slide 12: Flight Simulator visibility / windows plot
First step
- Evaluate Design Eye Point (DEP) and PEP and CEP
- Flight Simulator Visual System Eye point needs to correspond to Cockpit Eye Point
- Evaluation of Viewing Volume
- Evaluate visibility plot from PEP and CEP (if they are not same)
-cockpit windows coverage with projected image
- number of projected channels
- projectors and lenses
- blending solution

## Slide 13: Flight Simulator visibility / windows plot
Information from internet
Collimated flight simulators covering FOV with 3 – 5 channels with optional additional chin windows channel

## Slide 14: Flight Simulator visibility / windows plot
Information from internet
Direct projection flight simulators covering FOV with 8 – 10 channels with optional chin windows channel

## Slide 15: Flight Simulator Collimated Display Systems
Information from internet
Collimated flight simulators covering FOV with 3 – 5 ( or more) channels with optional additional chin windows channels
Collimating mirror/s
- Spherical or surface
- Mylar - Chips bag material
- Glass mirror
Projection screen
- Acrylic material
- Generally spherical or toroidal surface
- Back Projection Coating

## Slide 16: Flight Simulator Collimated Display Systems
Information from internet
Mylar - Chips bag material

## Slide 17: Flight Simulator Direct Projection Display Systems
Information from internet (RSI and RC)
Direct projection flight simulators covering FOV with 8 – 10 channels with optional chin windows channel
Projection screen
- Numbers of element depend of FOV
- Spherical surface
- Generally Front Projection Coating

## Slide 18: Flight Simulator Projection System
Information from internet
Projection system – Projectors using different technology
CRT (Cathode Ray Tube)
Absolete
Pro | Cons
Black is black (good black level) (optical blending not required) | Very big and heavy
Small light point size | Demanding alignment (3 lenses per projector)
Calligraphic light point | Low brightness
No Smearing | High maintenance required
LCoS (Liquid Cristal on Silicon)
DLP (Digital Light Processing)
LED (Light Emitting Diode)
Pro | Cons
High resolution | Black is not black (optical blending required)
High brightness (DLP , LCoS) Higher brightness than CRT (LED) | Cross reflection; baffles required
Better weight | Smear reduction needed (retinal smearing)
Lower maintenance | 

## Slide 19: Flight Simulator Projection System
Information from internet
Projection system – Projectors using different technology
Laser Hybrid technology
- 4 K resolution (4096 x 2160)
- Different supplier using a deferent approach
- Native 4K
- WQXGA (2560 x 1600) with shift
Speckle pattern

## Slide 20: Flight Simulator Projection System
Information from internet
Laser Hybrid technology A lot of options
RGB Laser (DLP)
RGB Laser (LCD/LCOS)
Laser/Phosphor (DLP)
Laser/Phosphor (LCD/LCOS)
Laser/LED Hybrid (DLP)

## Slide 21: Flight Simulator optical blending
Information from internet
2 channels overlap
4 channels overlap
3 channels overlap
Intensity brightness
channels dimesions
2 channels
No channels overlap
4 channels
3 channels

## Slide 22: Flight Simulator optical blending
Information from internet
Blend zones optical and electronic blending
Intensity brightness

## Slide 23: Flight Simulator optical smearing
Information from internet

## Slide 24: Flight Simulator Industry
Information from internet
Very large domain giving a lot of possibilities for physicists